## Slide 1: Lab2 Intro Improving Performance
Vivado HLS 2015.4 Version

## Slide 2: Objectives
After completing this lab, you will be able to:
  Add directives to your design
  Understand the effect of INLINE-ing functions
  Observe the effect of PIPELINE-ing functions
  Improve the performance using various directives

## Slide 3: The Design
The design consists of YUV filter typically used in video processing. The design consists of three functions – rgb2yuv, yuv_scale, and yuv2rgb
  Each of these functions iterates over the entire source image, requiring a single source pixel to produce a pixel in the result image
  The scale function simply applies individual scale factors, supplied through top-level arguments

## Slide 4: Procedure
Create a Vivado HLS project by executing script from Vivado HLS command prompt
Open the created project in Vivado HLS GUI and analyze
Apply TRIPCOUNT directive using PRAGMA
Apply PIPELINE directive, generate solution, and analyze output
Apply DATAFLOW directive to improve performance
Export and Implement the design

## Slide 5: Summary
In this lab you learned that even though this design could not be pipelined at the top-level, a strategy of pipelining the individual loops and then using dataflow optimization to make the functions operate in parallel was able to achieve the same high throughput, processing one pixel per clock. When DATAFLOW directive is applied, the default memory buffers (of ping-pong type) are automatically inserted between the functions. Using the fact that the design used only sequential (streaming) data accesses allowed the costly memory buffers associated with dataflow optimization to be replaced with simple 2 element FIFOs using the Dataflow command configuration