## Slide 1: Creating Processor System
Vivado HLS 2015.4 Version

## Slide 2: Objectives
After completing this module, you will be able to:
  Describe embedded system development flow in Zynq
  List the steps involved in creating hardware accelerator
  State how hardware accelerator created in Vivado HLS is used in Vivado Design Suite

## Slide 3: Outline
Embedded System Design in Zynq using IP Integrator
Creating IP-XACT Hardware Accelerator
Integrating the IP-XACT Hardware Accelerator in AXI System
Summary

## Slide 4: Embedded Design Architecture in Zynq
Embedded design in Zynq is based on:
  Processor and peripherals
    Dual ARM® Cortex™ -A9 processors of Zynq-7000 AP SoC
    AXI interconnect
    AXI component peripherals
    Reset, clocking, debug ports
  Software platform for processing system
    Standalone OS
    C language support
    Processor services
    C drivers for hardware
  User application
    Interrupt service routines (optional)

## Slide 5: The PS and the PL
The Zynq-7000 AP SoC architecture consists of two major sections
  PS: Processing system
    Dual ARM Cortex-A9 processor based
    Multiple peripherals
    Hard silicon core
  PL: Programmable logic
    Uses the same 7 series programmable logic
      Artix™-based devices: Z-7010, Z-7015, and Z-7020 (high-range I/O banks only)
      Kintex™-based devices: Z-7030, Z-7035, Z-7045, and Z-7100 (mix of high-range and high-performance I/O banks)

## Slide 6: Vivado
What are Vivado, IP Integrator and SDK?
  Vivado is the tool suite for Xilinx FPGA design and includes capability for embedded system design
    IP Integrator, is part of Vivado and allows block level design of the hardware part of an Embedded system
    Integrated into Vivado
    Vivado includes all the tools, IP, and documentation that are required for designing systems with the Zynq-7000 AP SoC hard core and/or Xilinx MicroBlaze soft core processor
    Vivado + IPI replaces ISE/EDK
  SDK is an Eclipse-based software design environment
    Enables the integration of hardware and software components
    Links from Vivado
Vivado is the overall project manager and is used for developing non-embedded hardware and instantiating embedded systems
  Vivado/IP Integrator flow is recommended for developing Zynq embedded systems

## Slide 7: Embedded System Tools: Hardware
Hardware development tools
  IP Integrator
  IP Packager
  Hardware netlist generation
  Simulation model generation
  Hardware debugging using Vivado analyzer cores

## Slide 8: Embedded System Tools: Software
Eclipse IDE-based Software Development Kit (SDK)
  Board support package creation
  GNU software development tools
  C/C++ compiler for the MicroBlaze and ARM Cortex-A9 processors (gcc)
  Debugger for the MicroBlaze and ARM Cortex-A9 processors (gdb)
  TCF framework – multicore debug
Board support packages (BSPs)
  Stand-alone BSP
    Free basic device drivers and utilities from Xilinx
    NOT an RTOS

## Slide 9: Vivado View
Customizable panels
A: Project Management
B: IP Integrator
C: FPGA Flow
D: Layout Selection
E: Project view/Preview Panel
F: Console, Messages, Logs
A
B
C
D
E
F

## Slide 10: Embedded System Design using Vivado
13. Program bitstream & .elf into Zynq
Vivado
Hardware Configuration
IP Integrator
SDK
2. Invoke IP Integrator to create Block Diagram
5. Generate Top-Level HDL
6. Add Constraints
7. Generate Bitstream => .bit
8. Export hardware
9. Launch SDK
3. Configure PS settings
4. Add IP & configure
10. Specify hardware description from Vivado
11. Create Software Platform (BSP)
12. Create Software Project & Build => .elf
1. Launch Vivado
ZedBoard

## Slide 11: Add IP Integrator Block Diagram
IP Integrator Block Diagram opens a blank canvas
IP can be added from the IP catalog
Drag and drop interface
Intelligent Design environment
  Design Assistance
  Connection automation
  Highlights valid connections
  Group, create hierarchal blocks
Can import custom IP using IP Packager

## Slide 12: Configuring and Connecting Hardware in IP Integrator
Double click blocks to access configuration options
Drag pointer to make connections
  Highlights valid connections
Connection Automation
  Automatically connect recognised interfaces
Automatically redraw system

## Slide 13: Exporting to XSDK
Export hardware first
  The Hardware Description File (hdf) format file containing all the relevant information will be created and placed under the *.sdk directory
  Include bitstream if generated
Launch XSDK
  Software development is performed with the Xilinx Software Development Kit tool (XSDK)
The XSDK tool will then associate user software projects to hardware

## Slide 14: Software Development Flow
Create/Import hardware platform project
  Automatically performed when XSDK tool is launched from Vivado project
Create BSP
  System software, board support package
Create software application
Update linker script, if needed
Build project
  compile, assemble, link output file <app_project>.elf

## Slide 15: Outline
Embedded System Design in Zynq using IP Integrator
Creating IP-XACT Hardware Accelerator
Integrating the IP-XACT Hardware Accelerator in AXI System
Summary

## Slide 16: Using RESOURCE for external connections
When the array is an argument of the top-level function
  The array/RAM is “off-chip”
  The type of RESOURCE determines the top-level IO ports
Default RAM resource
  Dual port RAM if performance can be improved otherwise Single Port RAM
Use RESOURCE directive on arrays in the model to use specific type of memory
Synthesis
foo_top
DOUT
DIN
ADDR
CE
WE
SPRAMB
A_out1
void foo_top( int A[3*N] , int x)
{
L1: for (i = 0; i < N; i++)
A[i+x] = A[i] + i;
}
+
Number of ports is defined by the RAM resource specified for array A[ ]

## Slide 17: Port-Level Interfaces
The AXI4 interfaces supported by Vivado HLS include
  The AXI4-Stream (axis)
    Specify on input arguments or output arguments only, not on input/output arguments
  The AXI4 master (m_axi)
    Specify on arrays and pointers (and references in C++) only. You can group multiple arguments into the same AXI4-Lite interface using the bundle option
  The AXI4-Lite (s_axilite)
    Specify on any type of argument except arrays. You can group multiple arguments into the same AXI4-Lite interface using the bundle option

## Slide 18: Interface Modes
Native AXI Interfaces
  AXI4 Slave Lite and AXI4 Master supported by INTERFACE directive
  Provided in RTL after Synthesis
  Supported by C/RTL Co-simulation
  Supported for Verilog and VHDL
BRAM Memory Interface
  Identical IO protocol to ap_memory
  Bundled differently in IP Integrator
    Provides easier integration to memories with BRAM interface
Scalar
Argument Type
Interface Mode
pass-by-value
pass-by-reference
pass-by-reference
ap_ctrl_none
ap_ctrl_hs
D
ap_ctrl_chain
axis
Supported. D = Default Interface
s_axilite
m_axi
ap_none
D
D
ap_stable
ap_ack
ap_vld
D
ap_ovld
D
ap_hs
ap_memory
D
D
D
bram
ap_fifo
ap_bus
Array
Pointer or Reference
Input
Return
I
IO
O
I
IO
O
Not Supported
axis
s_axilite
m_axi
bram

## Slide 19: Native AXI Slave Lite Interface
Interface Mode: s_axilite
  Supported with INTERFACE directive
  Multiple ports may be grouped into the same Slave Lite interface
    All ports which use the same bundle name are grouped
Grouped Ports
  Default mode is ap_none for input ports
  Default mode is ap_vld for output ports
  Default mode ap_ctrl_hs for function (return port)
  Default mode can be changed with additional INTERFACE directives
void example(char *a, char *b, char *c)
{
#pragma HLS INTERFACE s_axilite port=return bundle=BUS_A
#pragma HLS INTERFACE s_axilite port=a bundle=BUS_A
#pragma HLS INTERFACE s_axilite port=b bundle=BUS_A
#pragma HLS INTERFACE s_axilite port=c bundle=BUS_A
#pragma HLS INTERFACE ap_hs port=a
#pragma HLS INTERFACE ap_vld port=b
#pragma HLS INTERFACE ap_none port=c register

## Slide 20: Controllable Register Maps in AXI4 Lite
void hls_sig_gen_bram2axis(hls::stream<axis_last_t<data_t> >& dout,
data_t sig_buf[MAX_SIG_PERIOD], short sig_period)
{
#pragma HLS INTERFACE port=return s_axilite bundle=ctrl
#pragma HLS INTERFACE port=sig_buf s_axilite bundle=ctrl offset=0x1000
#pragma HLS INTERFACE port=sig_period s_axilite bundle=ctrl offset=0x0400
Assigning offset to array (RAM) interfaces
  Specified value is offset to base of array
  Array’s address space is always contiguous and linear
C Driver Files include offset information
  In generated driver file xhls_sig_gen_bram2axis.h
...
#define XHLS_SIG_GEN_BRAM2AXIS_CTRL_ADDR_SIG_PERIOD_DATA 0x0400
...
#define XHLS_SIG_GEN_BRAM2AXIS_CTRL_ADDR_SIG_BUF_BASE 0x1000
#define XHLS_SIG_GEN_BRAM2AXIS_CTRL_ADDR_SIG_BUF_HIGH 0x17ff
...
Page 20

## Slide 21: Native AXI4 Master
Interface Mode: m_axi
  Supported with INTERFACE directive
Options
  Multiple ports may be grouped into the same AXI4 Master interface
    All ports which use the same bundle name are grouped
  Depth option is required for C/RTL co-simulation
    Required for pointers, not arrays
    Set to the number of values read/written
  Option to support offset or base address
void example(volatile int *a)
{
#pragma HLS INTERFACE m_axi depth=50 port=a

## Slide 22: Native AXI4 Master : Offset Support
Address Offset / Base Address Support
  Support provided for address offset
Port Offset
  Defines the offset for the port
  May be set on individual interfaces using the INTERFACE directive
Global Offset
  Globally controls the offset ports of all M_AXI interface in the design
  May be set using the interface configuration
    Using Tcl command config_interface -m_axi_offset option

## Slide 23: Native AXI4 Master: Offset=off (default)
Default AXI4 Master Interface
  No offset is provided for the address
    Same as existing behavior
  The offset (BASEADDR) is set IPI
    Using IP customization GUI
  The offset can not be changed on the fly
config_interface -m_axi_offset off
AXI4 Master Interface

## Slide 24: Native AXI4 Master: Offset=direct
Direct Interface
  Generates a scalar input offset port
  The offset is set by driving the input port
  It can be changed on the fly by driving the port with a different value
AXI4 Master Interface …
config_interface -m_axi_offset direct
…Plus port to specify address offset

## Slide 25: Native AXI4 Master: Offset=slave
Direct Interface
  Generates an offset port and automatically maps it to an AXI4 Slave Lite interface
  User must program the offset before starting transactions on the AXI4 Master interface
  It can changed on the fly by re-programming the offset register
AXI4 Master Interface …
config_interface -m_axi_offset slave
…Plus AXI4 Slave Lite interface to program the address offset

## Slide 26: Burst Accesses Inferred for AXI4 Master
There are two types of accesses on an AXI Master
  Burst accesses are more efficient
  Burst access has until now required the use of memcpy()
Burst Accesses are now inferred
  From operations in a for-loop and from sequential operations in the code
  However: there are some limitations
    Single for-loops only, no nested loops
Single Access
Burst Access
void example(int *a)
{
#pragma HLS INTERFACE m_axi port=a depth=...
...
int val[i] = *(a + i);
...
void example(int *a)
{
#pragma HLS INTERFACE m_axi port=a depth=...
...
memcpy(vals, a, N * sizeof(int));
...
Page 26

## Slide 27: Byte-Enable Accesses on AXI4 Master
Byte-Enable Accesses Support on AXI4 Master Interfaces
  Single bytes are now written and read
  Improved AXI4 Master performance
Improved Performance
  This code uses 8-bit data
    Previously, accessing this required reading/writing full 32-bit
    This implied a required read-modify-write behavior: Impacted performance
  Similar performance improvement when accessing struct members
    Also often implied read-modify-write behavior
  Improved Port Bundling
    Variables of different sizes can be grouped into same AXI4 Master port
void example(volatile char *a) {
#pragma HLS INTERFACE m_axi depth=50 port=a
Page 27

## Slide 28: AXI4 Master Interface: Pipeline Support
Transaction involving an AXI4 Master Interface is now Pipelined
  Prior to 2015.4 this interface would not pipeline
  Each transfer was an “atomic” process
    The for-loop/memcpy waits until a transfer completes before starting next transfer
    This was the limiting factor in the pipeline interval
Improved performance in 2015.4
  Accesses to an AXI master interface can now be pipelined
    The performance will be much better than before

## Slide 29: AXI4 Port Bundling
AXI4 Master and Lite Port Bundling
  The bundle options groups arguments into the same AXI4 port
  For example, group 3 arguments into AXI4 port “ctrl” :
Arguments can be Bundled into AXI4 Master and AXI4 Lite ports
  If no bundle name is used a default name is used for all arguments
    All go into a single AXI4 Master or AXI4 Lite
    Default name applied if no –bundle option is used
  Group different sized variables into an AXI4 Master port
void hls_sig_gen_bram2axis(hls::stream<data_t>& dout,
data_t sig_buf[MAX_SIG_PERIOD], short sig_period)
{
#pragma HLS INTERFACE port=return s_axilite bundle=ctrl
#pragma HLS INTERFACE port=sig_buf s_axilite bundle=ctrl
#pragma HLS INTERFACE port=sig_period s_axilite bundle=ctrl
#pragma HLS INTERFACE port=dout axis

## Slide 30: AXI4 Stream Interface: Ease of Use
Native Support for AXI4 Stream Interfaces
  Native = An AXI4 Stream can be specified with set_directive_interface
    No longer required to set the interface then add a resource
    This AXI4 Stream interface is part of the HDL after synthesis
    This AXI4 Stream interface is simulated by RTL co-simulation
Interface Type “axis” is AXI4 Stream
set_directive_interface –mode axis “foo” portA
Or
#pragma HLS interface axis port=portA

## Slide 31: Generate the hardware accelerator
Select Solution > Export RTL
Select IP Catalog, System Generator for Vivado or PCore for EDK
Click on Configuration… if you want to change the version number or other information
  Default is v1_00_a
Click on OK
  The directory (ip) will be generated under the impl folder under the current project directory and current solution
  RTL code will be generated, both for Verilog and VHDL languages in their respective folders

## Slide 32: Generated impl Directory
Point IP Catalog to point to the ip directory
Generated Verilog RTL Files
Header file for slave interfaces
IP Integrator will use this file
XSDK will use this directory

## Slide 33: C Driver API for AXI4-Lite Interface

## Slide 34: Outline
Embedded System Design in Zynq using IP Integrator
Creating IP-XACT Hardware Accelerator
Integrating the IP-XACT Hardware Accelerator in AXI System
Summary

## Slide 35: Embedded System Design using Vivado
Create a new Vivado project, or open an existing project
Invoke IP Integrator
Construct(modify) the hardware portion of the embedded design by adding the IP-XACT hardware accelerator created in Vivado HLS
Create (Update) top level HDL wrapper
Synthesize any non-embedded components and implement in Vivado
Export the hardware description, and launch XSDK
Create a new software board support package and application projects in the XSDK
Compile the software with the GNU cross-compiler in XSDK
Download the programmable logic’s completed bitstream using Xilinx Tools > Program FPGA in XSDK
Use XSDK to download and execute the program (the ELF file)

## Slide 36: Outline
Embedded System Design in Zynq using IP Integrator
Creating IP-XACT Hardware Accelerator
Integrating the IP-XACT Hardware Accelerator in AXI System
Summary

## Slide 37: Summary
Embedded system development flow in FPGA involves
  Developing hardware using IP Integrator and Vivado
  Developing software using XSDK
hardware accelerator provides wide support of AXI interfaces, System Generator design, and Pcore for EDK
  Use the INTERFACE directive
  The choice of hardware accelerator is a function of the C variable type (pointer, etc.)
Start with the correct C argument type
  Verify the design at the C level
  Accept the default block-level I/O protocol
  Select the port-level I/O protocol that gives the required hardware accelerator interface
  Optionally group ports