## Slide 1: Improving Area and Resources
Vivado HLS 2015.4 Version

## Slide 2: Objectives
After completing this module, you will be able to:
  Describe how arbitrary precision data types can reduce resource utilization
  List various area optimization techniques
  List means by which resource utilization can be reduced

## Slide 3: Outline
Optimizing Resource Utilization
Reducing Area Usage
Summary

## Slide 4: Review: Control Scheduling & Binding
Scheduling & Binding
  Scheduling and Binding are the processes at the heart of HLS
Binding configuration
  Can be used to minimize the number of operations
The allocation directive
  Can be used to limit the number of operation in scheduling & binding stages
The resource directive
  Can be used to specify which cores are to be used during binding

## Slide 5: Configuring Binding
Binding is controlled via a configuration command
  The effort levels determine how much time is spent trying to map many operators onto fewer cores
  As with all effort levels, they are worth using if you can see the design close to what is required
    Else the tool will spend time exploring for possibilities
    And simply increase run time
    Use efforts judiciously
Binding can be configured to minimize specific operators
  Can be used to direct Vivado HLS to synthesize with the minimum number of operations
  The configuration command overrides muxing costs and can be used to force sharing
    Works on all scopes in a design
Operators which can be minimized
• add - Addition
• sub - Subtraction
• mul - Multiplication
• icmp - Integer Compare
• sdiv - Signed Division
• udiv - Unsigned Division
• srem - Signed Remainder
• urem - Unsigned Remainder
• lshr - Logical Shift-Right
• ashr - Arithmetic Shift-Right
• shl - Shift-Left

## Slide 6: Allocation: Limit the Numbers
Allocation directive limits different types
  Type: Operation
    The instances are the operators
    Add, mul, urem, etc.
  Type: Core
    The instances are the cores
    Adder, Addsub, PipeMult2s, etc
  Type: Functions
    The functions in the code
    Discussed in more detail later
Allocations are defined for a scope
  Like all directives, allocations are set for the scope they are applied in
    If the directive is applied to a function, loop or region, it does not include objects outside that scope
Operators and Cores are listed in the Vivado HLS Library Guide
21- 6

## Slide 7: Additional Control: Specify Resources
User control of Resources
  The resource directive gives user control over the specific resource (core) used to implement operations
    Select the scope & right-click to apply the directive
    Select “core” for a list of resources
    Specify the variable
Multiple line coding caveat
  If multiple operations occur on a single line
  A temporary variable is required to isolate the specific operation
In this example, “data” is implemented with a 2-stage pipelined multiplier
    a=b*c*d
    data= c*d;
    a = b*data;

## Slide 8: Outline
Optimizing Resource Utilization
Reducing Area Usage
Summary

## Slide 9: Improving Area/Resource Utilization
Control the number of elements
  Directives can be used to control scheduling and binding
Control the design hierarchy
  Like RTL synthesis, removing the hierarchy can help optimize across function and loop boundaries
    Functions can be inlined
    Loops can be unrolled
Array implementation
  Vivado HLS provides directives for combining memories
    Allowing a single large memory to be used instead of multiple smaller memories
Bit-width optimization
  Arbitrary precision types ensure correct operator sizing

## Slide 10: Review: Functions & RTL Hierarchy
Each function is translated into an RTL block
  Verilog module, VHDL entity
void A() { ..body A..}
void B() { ..body B..}
void C() {
B();
}
void D() {
B();
}
void foo_top() {
A(…);
C(…);
D(…)
}
foo_top
A
C
B
D
B
Source Code
RTL hierarchy
my_code.c
Functions can be inlined – the hierarchy removed & the function dissolved into the surrounding function
21- 10

## Slide 11: Controlling Inlining
Vivado HLS performs some inlining automatically
  This is performed on small logic functions if Vivado HLS determines area or performance will benefit
User Control
  Functions can be specifically inlined
    The function itself is inlined
  Optionally recursively down the hierarchy
  Optionally everything within a region can be inlined
    Everything named region or a function or a loop
  Optionally inlining can be explicitly prevented
    Turn inlining off
Inlining functions allows for greater optimization
  Like ungrouping RTL hierarchies: optimization across boundaries
  Like ungrouping RTL hierarchies it can result in lots of operations & impact run time
21- 11

## Slide 12: Function Inlining
sumsub_func
sumsub_func
shift_func
A
+
-
B
+
-
>>2
>>1
add_sub_pass
Inlining can be used to remove function hierarchy
int sumsub_func (int *in1, int *in2, int *outSum, int *outSub) {
*outSum = *in1 + *in2;
*outSub = *in1 - *in2;
}
int shift_func (int *in1, int *in2, int *outA, int *outB) {
*outA = *in1 >> 1;
*outB = *in2 >> 2;
}
void add_sub_pass(int A, int B, int *C, int *D) {
int apb, amb;
int a2, b2;
sumsub_func(&A,&B,&apb,&amb);
sumsub_func(&apb,&amb,&a2,&b2);
shift_func(&a2,&b2,C,D);
}
add_sub_pass
A
B
A
B>>1
Zero Area
Inlining allows optimization to be performed across function hierarchies
No Inlining
Inlining
2 Adders
2 Subtractors
A+B
A-B
Like RTL ungrouping, too much inlining can create a lot of logic and slow runtime
A+B
A-B
2A
A+B
A-B
2B
+
-
A
B>>1
21- 12

## Slide 13: Inline and Allocation: Shape the Hierarchy
One RTL block is reused for both instances of function foo
Easy to Share
Function foo is not within the immediate scope of foo_top
Cannot be shared
Inlining brings foo into function foo_top where it can be shared
Controlling Sharing
21- 13

## Slide 14: Loops
By default, loops are rolled
  Each C loop iteration  Implemented in the same state
  Each C loop iteration  Implemented with same resources
For Area optimization
void foo_top (…) {
...
Add: for (i=3;i>=0;i--) {
b = a[i] + b;
...
}
foo_top
+
Synthesis
N
a[N]
b
Keeping loops rolled maximizes sharing across loop iterations: each iteration of the loop uses the same hardware resources
21- 14

## Slide 15: Loop Merging & Flattening
Loop merging & flattening can remove the redundant computation among multiple (related) loops
  Improving area (and sometimes performance)
Allows Vivado HLS to perform optimizations
  Optimization cannot occur across loop boundaries
My_Region: {
#pragma HLS merge loop
for (i = 0; i < N; ++i) A[i] = B[i] + 1;
for (i = 0; i < N; ++i) C[i] = A[i] / 2;
}
for (i = 0; i < N; ++i) { A[i] = B[i] + 1; C[i] = A[i] / 2; }
Merge
Removes A[i], any address logic and any potential memory accesses
for (i = 0; i < N; ++i) C[i] = (B[i] + 1) / 2;
Effective code after compiler transformation
21- 15

## Slide 16: Mapping Arrays
The arrays in the C model may not be ideal for the available RAMs
  The code may have many small arrays
  The array may not utilize the RAMs very well
Array Mapping
  Mapping combines smaller arrays into larger arrays
    Allows arrays to be reconfigured without code edits
  Specify the array variable to be mapped
  Give all arrays to be combined the same instance name
Vivado HLS provides options as to the type of mapping
  Combine the arrays without impacting performance
    Vertical & Horizontal mapping
Global Arrays
  When a global array is mapped all arrays involved are promoted to global
  When arrays are in different functions, the target becomes global
Arrays which are function arguments
  All must be part of the same function interface
21- 16

## Slide 17: Horizontal Mapping
Horizontal Mapping
  Combines multiple arrays into longer (horizontal) array
  Optionally allows the arrays to be offset
    The default is to concatenate after the last element
    The first array specified (in GUI or Tcl script) starts at location zero
21- 17

## Slide 18: Vertical Mapping
Vertical Mapping
  Combines multiple arrays in to an array with more bits
  The first array specified (in Tcl or GUI) starts at the LSB
Vertical Mapping for performance
  Creates RAMs with wide words  Parallel accesses
21- 18

## Slide 19: Arbitrary Precision Integers
C and C++ have standard types created on the 8-bit boundary
  char (8-bit), short (16-bit), int (32-bit), long long (64-bit)
    Also provides stdint.h (for C), and stdint.h and cstdint (for C++)
    Types: int8_t, uint16_t, uint32_t, int_64_t etc.
  They result in hardware which is not bit-accurate and can give sub-standard QoR
Vivado HLS provides bit-accurate types in both C and C++
  Plus SystemC types can be used in C++
  Allow any arbitrary bit-width to be specified
  Will simulate with bit-accuracy
21- 19

## Slide 20: Why are Arbitrary Precision types Needed?
Code using native C int type
However, if the inputs will only have a max range of 8-bit
  Arbitrary precision data-types should be used
  It will result in smaller & faster hardware with full precision
21- 20

## Slide 21: Outline
Optimizing Resource Utilization
Reducing Area Usage
Summary

## Slide 22: Summary
Resource utilization can be reduced using allocation and binding controls
Arbitrary precision data types help controlling both the area and resource utilization
The design structure can be controlled by
  Inlining functions: direct impact on RTL hierarchy & optimization possibilities
  Loops: direct impact on reuse of resources
  Arrays: direct impact on the RAM
Major area optimization techniques
  Minimize bit widths
  Map smaller arrays into larger arrays
    Make better use of existing RAMs
  Control loop hierarchy
  Control function call hierarchy
  Control the number of operators and cores