## Slide 1: Data Types
Vivado HLS 2015.4 Version

## Slide 2: Objectives
After completing this module, you will be able to:
  State various data types of C, C++, and SystemC are supported
  Identify advantages and pitfalls of using arbitrary precision
  List various supported quantization and overflow modes
  Describe the floating point support

## Slide 3: Outline
C and C++ Data Types
Arbitrary Precision Data Types
System C Data Types
Floating Point Support
Summary

## Slide 4: Data Types and Bit-Accuracy
C and C++ have standard types created on the 8-bit boundary
  char (8-bit), short (16-bit), int (32-bit), long long (64-bit)
    Also provides stdint.h (for C), and stdint.h and cstdint (for C++)
    Types: int8_t, uint16_t, uint32_t, int_64_t etc.
  They result in hardware which is not bit-accurate and can give sub-standard QoR
Vivado HLS provides bit-accurate types in both C and C++
  Allow any arbitrary bit-width to be specified
  Hence designers can improve the QoR of the hardware by specifying exact data widths
    Can be specified in the code and simulated to ensure there is no loss of accuracy
14- 4

## Slide 5: Why is arbitrary precision Needed?
Code using native C int type
However, if the inputs will only have a max range of 8-bit
  Arbitrary precision data-types should be used
  It will result in smaller & faster hardware with the full required precision
  With arbitrary precision types on function interfaces, Vivado HLS can propagate the correct bit-widths throughout the design

## Slide 6: HLS & C Types
There are 4 basic types you can use for HLS
  Standard C/C++ Types
  Vivado HLS enhancements to C: apint
  Vivado HLS enhancements to C++: ap_int, ap_fixed
  SystemC types
14- 6

## Slide 7: Outline
C and C++ Data Types
Arbitrary Precision Data Types
System C Data Types
Floating Point Support
Summary

## Slide 8: Arbitrary Precision : C apint types
For C
  Vivado HLS types apint can be used
  Range: 1 to 1024 bits
  Specify the integers as shown and just use them like any other variable
There are two issues to be aware of
  C compilation : YOU MUST use apcc to simulate (no debugger support)
  Be aware of integer promotion issues
#include ap_cint.h
void foo_top (…) {
int9 var1; // 9-bit
uint10 var2; // 10-bit unsigned
Include header file
Failure to use apcc to compile the C will result in INCORRECT results
This only applies to C
NOT C++ or SystemC
14- 8

## Slide 9: Using apcc
apcc
  Command line compatible with gcc
  Required to support arbitrary precision for C
  Use apcc at the Vivado HLS CLI (shell)
  HLS uses apcc automatically when it sees arbitrary precision is used in C model
apcc understands bit-accurate types
  Once you create bit-accurate types you must re-validate the C
  It’s the only way to discover rounding and truncation issues
    It’s fast in C !!!
#include “ap_cint.h”
int3 ex_bit_accurate (
int3 x1,
int3 y1
) {
return x1+y1;
}
0
0
1
0
0
0
0
…
0
0
1
0
0
0
0
…
0
1
0
0
0
0
0
…
+
gcc simulation
2
2
4
0
1
0
0
1
0
1
0
0
+
apcc simulation
2
2
-4
x1
y1
return
Given: x1=2
y1=2
Simulates as hardware
shell> apcc –o my_test test.c test_tb.c

## Slide 10: Integer Promotion
Integer promotion
  The apcc utility must still obey standard C/gcc rules and protocols
  Integer promotion:
    If the operator result is a larger type 
    The result is promoted to the target type (on 8, 16, 32 or 64 boundaries)
0
0
0
0
0
1
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0
1
0
*
Result in Hex
65536
65536
0
a
b
Integer promotion promotes a*b to 32-bit then assigns this to tmp: the top-bits are lost
Solution: cast before the operation
tmp = (int36)a * (int36)b;
0
0
0
0
0
1
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0
0
1
*
4294967296
a
b
65536
65536
0
0
0
0
0
0
0
0
0
0
#include "ap_cint.h"
int36 mult (int18 a,int18 b) {
int36 tmp;
tmp = a * b;
return tmp;
}
Given: a=0x10000
b=0x10000

## Slide 11: C apint types: Bit-Selection & Manipulation
Function |  | Example
Length | Returns the length of the variable. | res=apint_bitwidthof(var);
Concatenation | Concatenation low to high | res=apint_concatenate(var_high, var_low)
Get a range | Return a bit-range from high to low. | res= apint_get_range(var, high,low)
Set a range | Reserve the bits in the variable | apint_set_range(res, high, low, res)
(n)and_reduce | (N)And reduce all bits. | bool t = apint_(n)and_reduce(var);
(n)or_reduce | (N)Or reduce all bits | bool t = apint_(n)or_reduce(var);
X(n)or_reduce | X(N)or reduce all bits | bool t = apint_x(n)or_reduce(var);
Get a bit | Get a specific bit | res=apint_get_bit(var, bit-number)
Set bit value | Sets the value of a specific bit | apint_set_bit(res, bit-number)
Print value | Print the value of an apint variable | apint_print(int#N value, int radix));
Print value to file | Print the value of an apint variable to a file | apint_fprint(FILE* file, int#N value, int radix)
14- 11

## Slide 12: Arbitrary Precision : C++ ap_int types
For C++
  Vivado HLS types ap_int can be used
  Range: 1 to 1024 bits
      Signed: ap_int<W>
      Unsigned: ap_uint<W>
  The bit-width is specified by W
C++ compilation
  Use g++ at the Vivado HLS CLI (shell)
    Include the path to the Vivado HLS header file
#include ap_int.h
void foo_top (…) {
ap_int<9> var1; // 9-bit
ap_uint<10> var2; // 10-bit unsigned
Include header file
shell> g++ –o my_test test.c test_tb.c -I$VIVADO_HLS_HOME/include
14- 12

## Slide 13: Microsoft Visual Studio Support
C++ Arbitrary Precision Types are supported in Microsoft Visual Studio Compiler
  Simply include the Vivado HLS directory $(VIVADO_HLS_HOME)/include
  Note: C designs using arbitrary precision types (apint) must still use apcc
C++ Designs using AP_INT types
  In the MVS Project
    Click Project
    Click Properties
    In the panel that shows up, select C/C++
    Select general
    Click on additional include directories and add the path
14- 13

## Slide 14: AP_INT operators & conversions
Fully Supported for all Arithmetic operator
Methods for type conversion
Operations | 
Arithmetic | + - * / % ++ --
Logical | ~ !
Bitwise | & ¦ ^
Relational | > < <= >= == !=
Assignment | *= /= %= += -= <<= >>= &= ^= ¦=
Methods |  | Example
To integer | Convert to a integer type | res = var.to_int();
To unsigned integer | Convert to an unsigned integer type | res = var.to_uint();
To 64-bit integer | Convert to a 64-bit long long type | res = var.to_int64();
To 64-bit unsigned integer | Convert to an unsigned long long type | res = var.to_uint64();
To double | Convert to double type | res = var.double();
14- 14

## Slide 15: AP_INT Bit Manipulation methods
Methods |  | Example
Length | Returns the length of the variable. | res=var.length;
Concatenation | Concatenation low to high | res=var_hi.concat(var_lo); Or res= (var_hi,var_lo)
Range or Bit-select | Return a bit-range from high to low or a specific bit. | res=var.range(high bit,low bit); Or res=var[bit-number]
(n)and_reduce | (N)And reduce all bits. | bool t = var.and_reduce();
(n)or_reduce | (N)Or reduce all bits | bool t = var.or_reduce();
X(n)or_reduce | X(N)or reduce all bits | bool t = var.xor_reduce();
Reverse | Reserve the bits in the variable | var.reverse();
Test bit | Tests if a bit is true | bool t = var.test(bit-number)
Set bit value | Sets the value of a specific bit | var.set_bit(bit-number, value)
Set bit | Set a specific bit to one | var.set(bit-number);
Clear bit | Clear a specific bit to zero | var.clear(bit-number);
Invert Bit | Invert a specific bit | var.invert(bit-number);
Rotate right | Rotate the N-bits to the right | var.rrotate(N);
Rotate left | Rotate the N-bits to the left | var.lrotate(N);
Bitwise Invert | Invert all bits | var.b_not();
Test sign | Test if the sign is negative (return true) | bool t = var.sign();
14- 15

## Slide 16: Arbitrary Precision : C++ ap_fixed types
Support for fixed point datatypes in C++
  Include the path to the ap_fixed.h header file
  Both signed (ap_fixed) and unsigned types (ap_ufixed)
Advantages of Fixed Point types
  The result of variables with different sizes is automatically taken care of
  The binary point is automatically aligned
    Quantization: Underflow is automatically handled
    Overflow: Saturation is automatically handled
#include ap_fixed.h
void foo_top (…) {
ap_fixed<9, 5, AP_RND_CONV, AP_SAT> var1; // 9-bit,
// 5 integer bits, 4 decimal places
ap_ufixed<10, 7, AP_RND_CONV, AP_SAT> var2; // 10-bit unsigned
// 7 integer bits, 3 decimal places
$VIVADO_HLS_HOME/include/ap_fixed.h
Alternatively, make the result variable large enough such that overflow or underflow does not occur
14- 16

## Slide 17: Definition of ap_fixed type
Fixed point types are specified by
  Total bit width (W)
  The number of integer bits (I)
  The quantization/rounding mode (Q)
  The overflow/saturation mode (O)
  The number of saturation bits
 | Description | 
W | Word length in bits | 
I | The number of bits used to represent the integer value (the number of bits above the decimal point) | 
Q | Quantization mode (modes detailed below) dictates the behavior when greater precision is generated than can be defined by the LSBs. | 
 | AP_Fixed Mode | Description
 | AP_RND | Rounding to plus infinity
 | AP_RND_ZERO | Rounding to zero
 | AP_RND_MIN_INF | Rounding to minus infinity
 | AP_RND_INF | Rounding to infinity
 | AP_RND_CONV | Convergent rounding
 | AP_TRN | Truncation to minus infinity
 | AP_TRN_ZERO | Truncation to zero (default)
O | Overflow mode (modes detailed below) dictates the behavior when more bits are required than the word contains. | 
 | AP_Fixed Mode | Description
 | AP_SAT | Saturation
 | AP_SAT_ZERO | Saturation to zero
 | AP_SAT_SYM | Symmetrical saturation
 | AP_WRAP | Wrap around (default)
 | AP_WRAP_SM | Sign magnitude wrap around
N | The number of saturation bits in wrap modes. | 
Binary point : W = I + B
ap_[u]fixed<W, I , Q, O , N>
I-1
-1
…
-B
1
0
…
14- 17

## Slide 18: Quantization Modes
Quantization mode
  Determines the behavior when an operation generates more precision in the LSBs than is available
Quantization Modes (rounding):
  AP_RND, AP_RND_MIN_IF, AP_RND_IF
  AP_RND_ZERO, AP_RND_CONV
Quantization Modes (truncation):
  AP_TRN, AP_TRN_ZERO
14- 18

## Slide 19: Quantization Modes: Rounding
AP_RND_ZERO: rounding to zero
  For positive numbers, the redundant bits are truncated
  For negative numbers, add MSB of removed bits to the remaining bits.
  The effect is to round towards zero.
    01.01 (1.25 using 4 bits) rounds to 01.0 (1 using 3 bits)
    10.11 (-1.25 using 4 bits) rounds to 11.0 (-1 using 3 bits)
AP_RND_CONV: rounded to the nearest value
  The rounding depends on the least significant bit
  If the least significant bit is set, rounding towards plus infinity
  Otherwise, rounding towards minus infinity
    00.11 ( 0.75 using 4-bit) rounds to 01.0 (1.0 using 3-bit)
    10.11 (-1.25 using 4-bit) rounds to 11.0 (-1.0 using 3-bit)
14- 19

## Slide 20: Quantization Modes: Truncation
AP_TRN: truncate
  Remove redundant bits. Always rounds to minus infinity
  This is the default.
    01.01(1.25)  01.0 (1)
AP_TRN_ZERO: truncate to zero
  For positive numbers, the same as AP_TRN
    For positive numbers: 01.01(1.25)  01.0(1)
  For negative numbers, round to zero
    For negative numbers: 10.11 (-1.25)  11.0(-1)
14- 20

## Slide 21: Overflow Modes
Overflow mode
  Determines the behavior when an operation generates more bits than can be satisfied by the MSB
Overflow Modes (saturation)
  AP_SAT, AP_SAT_ZERO, AP_SAT_SYM
Overflow Modes (wrap)
  AP_WRAP, AP_WRAP_SM
  The number of saturation bits, N, is considered when wrapping
14- 21

## Slide 22: Overflow Mode: Saturation
AP_SAT: saturation
  This overflow mode will convert the specified value to MAX for an overflow or MIN for an underflow condition
  MAX and MIN are determined from the number of bits available
AP_SAT_ZERO: saturates to zero
  Will set the result to zero, if the result is out of range
AP_SAT_SYM: symmetrical saturation
  In 2’s complement notation one more negative value than positive value can be represented
  If it is desirable to have the absolute values of MIN and MAX symmetrical around zero, AP_SAT_SYM can be used
  Positive overflow will generate MAX and negative overflow will generate -MAX
    0110(6) => 011(3)
    1011(-5) => 101(-3)
14- 22

## Slide 23: Overflow Mode: Wrap Sign Magnitude
AP_WRAP_SM, N = 0
  This mode uses sign magnitude wrapping
  Sign bit set to the value of the least significant deleted bit
  If the most significant remaining bit is different from the original MSB, all the remaining bits are inverted
  IF MSBs are same, the other bits are copied over
    Step 1: First delete redundant MSBs. 0100(4) => 100(-4)
    Step 2: The new sign bit is the least significant bit of the deleted bits. 0 in this case
    Step 3: Compare the new sign bit with the sign of the new value
  If different, invert all the numbers. They are different in this case
    011 (3) 11
AP_WRAP_SM, N > 0
  Uses sign magnitude saturation
  Here N MSBs will be saturated to 1
  Behaves similar to case where N = 0, except that positive numbers stay positive and negative numbers stay negative
14- 23

## Slide 24: AP_FIXED operators & conversions
Fully Supported for all Arithmetic operator
Methods for type conversion
Operations | 
Arithmetic | + - * / % ++ --
Logical | ~ !
Bitwise | & ¦ ^
Relational | > < <= >= == !=
Assignment | *= /= %= += -= <<= >>= &= ^= ¦=
Methods |  | Example
To integer | Convert to a integer type | res = var.to_int();
To unsigned integer | Convert to an unsigned integer type | res = var.to_uint();
To 64-bit integer | Convert to a 64-bit long long type | res = var.to_int64();
To 64-bit unsigned integer | Convert to an unsigned long long type | res = var.to_uint64();
To double | Convert to double type | res = var.double();
To ap_int | Convert to an ap_int | res = var.to_ap_int();
14- 24

## Slide 25: AP_FIXED methods
Methods for bit manipulation
Methods |  | Example
Length | Returns the length of the variable. | res=var.length;
Concatenation | Concatenation low to high | res=var_hi.concat(var_lo); Or res= (var_hi,var_lo)
Range or Bit-select | Return a bit-range from high to low or a specific bit. | res=var.range(high bit,low bit); Or res=var[bit-number]
14- 25

## Slide 26: Fixed Point Math Functions
The hls_math.h library
  Now includes fixed-point functions for sin, cos and sqrt
    ULP- Units of Least Precision
  The sin and cos functions are all 32-bit ap_fixed<32,Int_Bit>
    Where Int_Bit specifies the number of integer bits
  The sqrt function is any width but must have a decimal point
    Cannot be all intergers or all bits
  The accuracy above is quoted with respect to the equivalent floating point version
Function | Type | Accuracy (ULP) | Implementation Style
cos | ap_fixed<32,I> | 16 | Synthesized
sin | ap_fixed<32,I> | 16 | Synthesized
sqrt | ap_fixed<W,I> ap_ufixed<W,I> | 1 | Synthesized

## Slide 27: Fixed Point Math Functions

## Slide 28: Outline
C and C++ Data Types
Arbitrary Precision Data Types
System C Data Types
Floating Point Support
Summary

## Slide 29: Arbitrary Precision : SystemC
SystemC is an IEEE standard (IEEE 1666)
  C++ class libraries
  Allows design and simulation with concurrency
  Provides a library of arbitrary precision types
    sc_int, sc_uint, sc_bigint (int > 64 bit), sc_fixed, etc.
SystemC support
  Vivado HLS supports SystemC 2.1 and 1.3 Synthesizable subset1
SystemC Compilation
  Compile with g++
  Include the SystemC files from the Vivado HLS tree
SC Types
  Can be used in C++ designs without the need to convert the entire design to SystemC
shell> g++ –o my_test test.c test_tb.c \
-I$Vivado HLS_HOME\Win_x86\tools\systemc\include \
-lsystemc \
-L$Vivado HLS_HOME\Win_x86\tools\systemc\include\lib

## Slide 30: Outline
C and C++ Data Types
Arbitrary Precision Data Types
System C Data Types
Floating Point Support
Summary

## Slide 31: Floating Point Support
Synthesis for floating point
  Data types (IEEE-754 standard compliant)
    Single-precision
      32 bit: 24-bit fraction, 8-bit exponent
    Double-precision
      64 bit: 53-bit fraction, 11-bit exponent
Support for Operators
  Vivado HLS supports the Floating Point (FP) cores for each Xilinx technology
    If Xilinx has a FP core, Vivado HLS supports it
    It will automatically be synthesized
  If there is no such FP core in the Xilinx technology, it will not be in the library
    The design will be still synthesized
14- 31

## Slide 32: Floating Point Cores
14- 32

## Slide 33: Outline
C and C++ Data Types
Arbitrary Precision Data Types
System C Data Types
Floating Point Support
Summary

## Slide 34: Summary
C and C++ have standard types created on the 8-bit boundary
  char (8-bit), short (16-bit), int (32-bit), long long (64-bit)
Vivado HLS supports SystemC 1.3 Synthesizable subset
Arbitrary precision in C is supported using apint and ap_int in C++
  Compile using apcc for arbitrary precision
  Arbitrary precision types can define bit-accurate operators leading to better QoR
Fixed point precision is supported in C++
  Both signed (ap_fixed) and unsigned types (ap_ufixed)

## Slide 35: Summary
Various quantization and overflow modes supported
  Quantization
    AP_RND, AP_RND_ZERO, AP_RND_MIN_INF, AP_RND_INF, AP_RND_CONV, AP_TRN, AP_TRN_ZERO
  Overflow
    AP_SAT, AP_SAT_ZERO, AP_SAT_SYM, AP_WRAP, AP_WRAP_SYM
Both single- and double-precision floating point data types are supported
  If a corresponding floating point core is available then it will automatically be used
  If floating point core is not available then Vivado HLS will generate the RTL model