## Slide 1: Block and Port Level Protocols
Vivado HLS 2015.4 Version

## Slide 2: Objectives
After completing this module, you will be able to:
  List the types of IO abstracted in Vivado HLS
  List various basic and optional IO ports handled in Vivado HLS
  State how a design can be synthesized as combinatorial and sequential
  Distinguish between block-level and port-level IO protocols
  State how pointer interfaces are implemented

## Slide 3: Outline
Introduction
Block Level Protocols
Port Level Protocols
Summary

## Slide 4: The Key Attributes of C code : IO
void fir (
data_t *y,
coef_t c[4],
data_t x
) {
static data_t shift_reg[4];
acc_t acc;
int i;
acc=0;
loop: for (i=3;i>=0;i--) {
if (i==0) {
acc+=x*c[0];
shift_reg[0]=x;
} else {
shift_reg[i]=shift_reg[i-1];
acc+=shift_reg[i] * c[i];
}
}
*y=acc>>2;
}
Code
Functions: All code is made up of functions which represent the design hierarchy: the same in hardware
Loops: Functions typically contain loops. How these are handled can have an impact on area and performance.
Arrays: Arrays are used often in C code. They can impact the device area and become performance bottlenecks.
Operators: Operators in the C code may require sharing to control area or be assigned to specific hardware implementations to meet performance
Types: All variables are of a defined type. The type can influence the area and performance
Input & Outputs: The arguments of the top-level function must be transformed to hardware interfaces with an IO protocol
22- 4

## Slide 5: Example 101 : Combinational Design
Simple Adder Example
  Output is the sum of 3 inputs
Synthesized with 100 ns clock
  All adders can fit in one clock cycle
  Combinational design
  The function return becomes RTL port ap_return
  No handshakes are required or created in this example
#include "adders.h"
int adders(int in1, int in2, int in3) {
int sum;
sum = in1 + in2 + in3;
return sum;
}
adders
ap_return
in1
In2
In3

## Slide 6: Example 102: Sequential Design
The same adder design is now synthesized with a 3ns clock
  The design now takes more than 1 cycle to complete
  Vivado HLS creates a sequential design with the default port types
By Default ..
  Block level handshake signals are added to the design
#include "adders.h"
int adders(int in1, int in2, int in3) {
int sum;
sum = in1 + in2 + in3;
return sum;
}
adders
ap_return
in1
In2
In3
Synthesis
ap_done
ap_start
ap_idle

## Slide 7: Vivado HLS IO Options
Vivado HLS has four types of IO
  Data ports created by the original top-level C function arguments
  IO protocol signals added at the Block-Level
  IO protocol signals added at the Port-Level
  IO protocol signals added externally as Pcore Interfaces
Data Ports
  These are the function arguments/parameters
Block-Level Interfaces (optional)
  An interface protocol which is added at the block level
  Controls the addition of block level control ports: start, idle, done, and ready
Port-Level interfaces (optional)
  IO interface protocols added to the individual function arguments
Pcore interfaces (optional)
  Added as external adapters when exported as an IP
22- 7

## Slide 8: Vivado HLS Basic Ports
Adder Example
#include "adders.h"
int adders(int in1, int in2, int *sum) {
int temp;
*sum = in1 + in2 + *sum;
temp = in1 + in2;
return temp;
}
adders
Synthesis
Clock added to all sequential RTL blocks
  One clock per function/block
  SystemC designs may have a unique clock for each CTHREAD
Reset added to all sequential RTL blocks
  Only the FSM and any variables initialized in the C are reset by default
  Reset and polarity options are controlled via the RTL Configuration
    Solutions/Solution Settings...
Optional Clock Enable
  An optional clock enable can be added via the sequential RTL configuration
  When de-asserted it will cause the block to “freeze”
    All connected blocks are assumed to be using the same CE
    When the IO protocol of this block freezes, it is expected other blocks do the same
    Else a valid output may be read multiple times
ap_clk
ap_rst
ap_ce
22- 8

## Slide 9: Vivado HLS Optional IO : Function Arguments
Adder Example
adders
sum_dataout
in1
in2
ap_return
sum_datain
Function Arguments
  Synthesized into data ports
Function Return
  Any return is synthesized into an output port called ap_return
Pointers (& C++ References)
  Can be read from and written to
  Separate input and output ports for pointer reads and writes
Arrays (not shown here)
  Like pointers can be synthesized into read and/or write ports
ap_clk
ap_rst
22- 9
#include "adders.h"
int adders(int in1, int in2, int *sum) {
int temp;
*sum = in1 + in2 + *sum;
temp = in1 + in2;
return temp;
}
adders
Synthesis

## Slide 10: Vivado HLS Optional IO : Block Level Protocol
Adder Example
sum_dataout
in1
in2
ap_done
ap_start
ap_idle
ap_return
sum_datain
Block Level Protocol
  An IO protocol added at the RTL block level
  Controls and indicates the operational status of the block
Block Operation Control
  Controls when the RTL block starts execution (ap_start)
  Indicates if the RTL block is idle (ap_idle) or has completed (ap_done)
Complete and function return
  The ap_done signal also indicates when any function return is valid
Ready (not shown here)
  If the function is pipelined an additional ready signal (ap_ready) is added
  Indicates a new sample can be supplied before done is asserted
adders
ap_clk
ap_rst
22- 10
#include "adders.h"
int adders(int in1, int in2, int *sum) {
int temp;
*sum = in1 + in2 + *sum;
temp = in1 + in2;
return temp;
}
Synthesis

## Slide 11: Vivado HLS Optional IO : Port IO Protocols
Adder Example
sum_dataout
in1
in2
ap_done
ap_start
ap_idle
ap_return
in1_ap_ack
in2_read
in1_ap_vld
in2_empty_n
sum_req_write
sum_rsp_read
sum_req_din
sum_address
sum_size
sum_req_full_n
sum_rsp_empty_n
sum_datain
Port IO Protocols
  An IO protocol added at the port level
  Sequences the data to/from the data port
Interface Synthesis
  The design is automatically synthesized to account for IO signals (enables, acknowledges etc.)
Select from a pre-defined list
  The IO protocol for each port can be selected from a list
  Allows the user to easily connect to surrounding blocks
Non-standard Interfaces
  Supported in C/C++ using an arbitrary protocol definition
  Supported natively in SystemC
adders
ap_clk
ap_rst
22- 11
#include "adders.h"
int adders(int in1, int in2, int *sum) {
int temp;
*sum = in1 + in2 + *sum;
temp = in1 + in2;
return temp;
}
adders
Synthesis

## Slide 12: Vivado HLS Interfaces Summary
Where do you find the summary?
  In the Synthesis report
Interface Summary Section (at the end)
The same pathname as this from the project directory
Ports
Sizes and Direction
22- 12

## Slide 13: Vivado HLS Optional IO : IP Adapters
Adder Example
Added when the IP block is exported
Available in the IP directory
  “ip”, “sysgen” or “pcore”
  AXI4LiteS
  AXI4
  AXI4Stream

## Slide 14: Outline
Introduction
Block Level Protocols
Port Level Protocols
Summary

## Slide 15: AP_START: Pulsed
Input Data
  Can be applied when ap_idle goes low
    The first read is performed 1 clock cycle after idle goes low
  Input reads can occur in any cycle up until the last cycle
Output Data
  Any function return is valid when ap_done is asserted high
  Other outputs may output their data at any time after the first read
    The output can only be guaranteed to be valid with ap_done if it is registered
    It is recommended to use a port level IO protocol for other outputs
The block will wait for ap_start before it begins operation
Output ap_idle goes low when ap_start is sampled high
Output ap_done goes high on the final cycle
Idle goes high one cycle after done
The block waits for next start

## Slide 16: AP_START: Constant High
Input and Output data operations
  As before
The key difference here is that the design is never idle
  The next data read is performed immediately
If start is high when done is asserted, the design will not enter the idle state
Since start is high, idle stays low
The block starts to execute the next transaction immediately

## Slide 17: Pipelined Designs
Input Data
  Will be read when ap_ready is high and ap_idle is low
    Indicates the design is ready for data
  Signal ap_ready will change at the rate of the II
Output Data
  As before, function return is valid when ap_done is asserted high
  Other outputs may output their data at any time after the first read
    It is recommended to use a port level IO protocol for other outputs
This example shows an II of 2
After reset, ap_ready goes high if idle is high
Start applied : Idle goes low, apply first data
Inputs will be read when ap_ready is high and idle is low
Output ap_done goes high on the final cycle
Idle goes high one cycle after done
The block waits for next start

## Slide 18: Pipelined Designs: II = 1
Input Data when II=1
  It can be expected that ap_ready remains high and data is continuously read
  The design will only stop processing when ap_start is de-asserted
Output Data when II=1
  After the first output, ap_done will remain high while there are samples to process
    Assuming there is no data decimation (output rate = input rate)
Will start with ap_start
Will keep reading input data since II = 1
After the first output, ap_done will remain high
If ap_start goes is sampled low, ap_ready will go low immediately

## Slide 19: Disabling Block Level Handshakes
Block Level Handshakes can be disabled
  Select the function in the directives tab, right-click
    Select Interface & then ap_ctrl_none for no block level handshakes
    Select Interface & then ap_ctrl_hs to re-apply the default
Requirement: Manually verify the RTL
  Without block level handshakes autosim cannot verify the design
    Will only work in simple combo and II=1 cases
    Handshakes are required to know when to sample output signals
# Tcl commands
set_directive_interface -mode ap_ctrl_none “dct“
# Default is on
# set_directive_interface -mode ap_ctrl_hs “dct“
It is recommended to leave the default and use Block Level Handshakes

## Slide 20: AP_CTRL_CHAIN
Protocol to support pipeline chains: ap_ctrl_chain
  Similar to ap_ctrl_hs but with additional signal ap_continue
  Allows blocks to be easily chained in a pipelined manner
  ap_ctrl_chain protocol provides back-pressure in systems

## Slide 21: AP_CTRL_CHAIN
Asserting the ap_continue signal Low informs the design that the downstream block that consumes the data is not ready to accept new data
When ap_continue is asserted Low, the design stalls when it reaches the final state of the current transaction: the output data is presented on the interface, the ap_done signal can be asserted High and the design remains in this state until ap_continue is asserted High

## Slide 22: Outline
Introduction
Block Level Protocols
Port Level Protocols
Summary

## Slide 23: Port Level IO protocols
We’ve seen how the function return is validated
  The block level output signal ap_done goes high to indicate the function return is valid
  This allows downstream blocks to correctly sample the output port
For other outputs, Port Level IO protocols can be added
  Allowing upstream and downstream blocks to synchronize with the other data ports
  The type of protocol depends on the type of C port
    Pass-by-value scalar
    Pass-by-reference pointers (& references in C++)
    Pass-by-reference arrays
adders
ap_return
in1
In2
In3
ap_done
ap_start
ap_idle
downstream
data
enable
sum
The starting point is the type of argument used by the C function

## Slide 24: Let’s Look at an Example
Key:
I : input
IO : inout
O : output
D : Default Interface
#include "adders.h"
int adders(int in1, int in2, int *sum) {
int temp;
*sum = in1 + in2 + *sum;
temp = in1 + in2;
return temp;
}
“Sum” is a pointer which is read and written to : an Inout
The port for “Sum” can be any of these interface types
The default for port for “Sum” will be type ap_ovld

## Slide 25: Interface Types
Multiple interface protocols
  Every combination of C argument and port protocol is not supported
  It may require a code modification to implement a specific IO protocol
Key:
I : input
IO : inout
O : output
D : Default Interface
No IO Protocol
Wire handshake protocols
Memory protocols : RAM
: FIFO
Bus protocols
Block Level Protocol
Block level protocols can be applied to the return port - but the port can be omitted and just the function name specified
22- 25

## Slide 26: Default IO Protocols
The default port protocols
  Inputs: ap_none
  Outputs: ap_vld
  Inout: ap_ovld
    In port gets ap_none
    Out port gets ap_vld
  Arrays: ap_memory
  All shown as the default (D) on previous slide
Result of the default protocols
  No protocol for input ports
    They should be held stable for the entire transaction
    There is no way to know when the input will be read
  Output writes have an accompanying output valid signal which can be used to validate them
  Arrays will default to RAM interfaces (2-port RAM is the default RAM)
The Vivado HLS shell/console always shows the results of interface synthesis
22- 26

## Slide 27: Specifying IO Protocols
Select the port in the Directives pane to specify a protocol
  Select the port
  Right-click and choose Interface
  Select the protocol from the drop-down menu
Or apply using Tcl or Pragma

## Slide 28: Interface Types
Multiple interface protocols
  Every combination of C argument and port protocol is not supported
  It may require a code modification to implement a specific IO protocol
Key:
I : input
IO : inout
O : output
D : Default Interface
No IO Protocol
Wire handshake protocols
Memory protocols : RAM
: FIFO
Bus protocols
Block Level Protocol
Block level protocols can be applied to the return port - but the port can be omitted and just the function name specified
22- 28

## Slide 29: No IO Protocol
AP_NONE: The default protocol for input ports
  Protocol ap_none means that no additional protocol signals are added
  The port will be implemented as just a data port
Other ports can be specified as ap_none
  Except arrays which must be a RAM or FIFO interface
AP_STABLE: An ap_none with fanout benefits
  The ap_stable type informs High-Level Synthesis that the data applied to this port remains stable during normal operation, but is not a constant value that could be optimized, and the port is not required to be registered
  Typically used for ports that provides configuration data - data that can change but remains stable during normal operation (configuration data is typically only changed during or before a reset)

## Slide 30: Interface Types
Multiple interface protocols
  Every combination of C argument and port protocol is not supported
  It may require a code modification to implement a specific IO protocol
Key:
I : input
IO : inout
O : output
D : Default Interface
No IO Protocol
Wire handshake protocols
Memory protocols : RAM
: FIFO
Bus protocols
Block Level Protocol
Block level protocols can be applied to the return port - but the port can be omitted and just the function name specified
22- 30

## Slide 31: Wire Protocols
The wire protocols add a valid and/or acknowledge port to each data port
The wire protocols are all derivatives of protocol ap_hs
  ap_ack: add an acknowledge port
  ap_vld: add a valid port
  ap_ovld: add a valid port to an output
  ap_hs: adds both
Output control signals are used to inform other blocks
  Data has been read at the input by this block (ack)
  Data is valid at the output (vld)
  The other block must accept the control signal (this block will continue)
Input control signals are used to inform this block
  The output data has been read by the consumer (ack)
  The input from the producer is valid (vld)
  This block will stall while waiting for the input controls

## Slide 32: Wire Protocols: Ports Generated
The wire protocols are all derivatives of protocol ap_hs
  Inputs
    Arguments which are only read
    The valid is input port indicating when to read
    Acknowledge is an output indicating it was read
  Outputs
    Arguments which are only written to
    Valid is an output indicating data is ready
    Acknowledge is an input indicating it was read
  Inouts
    Arguments which are read from and written to
    These are split into separate in and out ports
    Each half has handshakes as per Input and Output
foo
in1_ack
in1
in1_vld
foo
out1
out1_ack
adders
inout1_i_ack
inout1_i
Inout1_i_vld
Inout1_o_ack
out1_vld
inout1_o_vld
inout1_o
ap_hs is compatible with AXI-Stream
22- 32

## Slide 33: Handshake IO Protocol
After start, idle goes low and the RTL operates until a read is required
The RTL will stall (wait) until the input valid is asserted
If there is more than one input valid, each can stall the RTL
It will acknowledge on the same cycle it reads the data (reads on next clock edge)
An output valid is asserted when the port has data
The RTL will stall (hold the data and wait) until an input acknowledge is received
Done will be asserted when the function is complete
22- 33

## Slide 34: Other Handshake Protocols
The other wire protocols are derivatives of ap_hs in behavior
  Some subtleties are worth discussing when the full two-way handshake is not used
Using the Valid protocols (ap_vld, ap_ovld)
  Outputs: Without an associated input acknowledge it is a requirement that the consumer takes the data when the output valid is asserted
    Protocol ap_ovld only applies to output ports (is ignored on inputs)
  Inputs: No particular issue.
    Without an associated output acknowledge, the producer does not know when the data has been read (but the done signal can be used to update values)
Using the Acknowledge Protocol (ap_ack)
  Outputs: Without an associated output valid the consumer will not know when valid data is ready but the design will stall until it receives an acknowledge (Dangerous: Lock up potential)
  Inputs: Without an associated input valid, the design will simply read when it is ready and acknowledge that fact.

## Slide 35: Registering IO Reads and Writes
Vivado HLS does not register Input and Outputs by default
  It will chain operations to minimize latency
  The inputs will be read when the design requires them
  The outputs will be written as soon as they are available
Inputs and outputs can be registered
  Inputs will be registered in the first cycle
    Input pointers and partitioned arrays will be registered when they are required
  Outputs will be registered and held until the next write operation
    Which for scalars will be the next transaction (can’t write twice to the same port) unless the block is pipelined
in1
clk
in2
sum
sum
sum_vld
in3
X1
X2
X3
+
FD
+
22- 35

## Slide 36: Interface Types
Multiple interface protocols
  Every combination of C argument and port protocol is not supported
  It may require a code modification to implement a specific IO protocol
Key:
I : input
IO : inout
O : output
D : Default Interface
No IO Protocol
Wire handshake protocols
Memory protocols : RAM
: FIFO
Bus protocols
Block Level Protocol
Block level protocols can be applied to the return port - but the port can be omitted and just the function name specified
22- 36

## Slide 37: Memory IO Protocols
Memory protocols can be inferred from array and pointer arguments
  Array arguments can be synthesized to RAM or FIFO ports
    When FIFOs specified on array ports, the ports must be read-only or write-only
  Pointer (and References in C++) can be synthesized to FIFO ports
RAM ports
  Support arbitrary/random accesses
  May be implemented with Dual-Port RAMs to increase the bandwidth
    The default is a Dual-Port RAM interface
  Requires two cycles read access: generate address, read data
    Pipelining can reduce this overhead by overlapping generation with reading
FIFO ports
  Require read and writes to be sequential/streaming
  Always uses a standard FIFO (single-port) model
  Single cycle for both reads and writes
22- 37

## Slide 38: Memory IO Protocols: Ports Generated
RAM Ports
  Created by protocol ap_memory
  Given an array specified on the interface
  Ports are generated for data, address & control
    Example shows a single port RAM
    A dual-port resource will result in dual-port interface
  Specify the off-chip RAM as a Resource
    Use the RESOURCE directive on the array port
FIFO Ports
  Created by protocol ap_fifo
  Can be used on arrays, pointers and references
  Standard Read/Write, Full/Empty ports generated
    Arrays: must use separate arrays for read and write
    Pointers/References: split into In and Out ports
ram
d_d0
d_q0
d_address0
d_we0
d_ce0
#include "ram.h"
void ram (int d[DEPTH], …) {
…
}
#include "fifo.h"
void fifo (int d_o[DEPTH],
int d_i[DEPTH]) {
…
}
fifo
d_o_din
d_i_dout
d_o_write
d_i_read
d_i_empty_n
d_o_full_n
22- 38

## Slide 39: Memory IO Protocol (ap_memory)
There is no stall behavior initiated by a RAM interface
After start, idle goes low and the RTL operates
When a read is required, an address is generated and CE asserted high
Data is available on data input port d_q0 in the next cycle
The read operations may be pipelined
When a write is required, the address and data are placed on the output ports
Both CE &WE are asserted high
Writes may be pipelined
Done will be asserted when the function is complete
22- 39

## Slide 40: FIFO IO Protocol (ap_fifo, Read)
After start, idle goes low and the RTL operates until a read is required
The RTL will stall (wait) until the empty_n is asserted high to indicate data is available
As soon as data is available, the fifo read port will go high
Reads will occur when required, so long as data is available (empty_n is high)
22- 40

## Slide 41: FIFO IO Protocol (ap_fifo, Write)
When ready, data will be written to the output port
The RTL will then stall and hold the data until the FIFO is no longer full (full_n high)
As soon as data can written, write is asserted high
A write will occur when required if there is room in the fifo (full_n high)
Done will be asserted when the function is complete
22- 41

## Slide 42: Interface Types
Multiple interface protocols
  Every combination of C argument and port protocol is not supported
  It may require a code modification to implement a specific IO protocol
Key:
I : input
IO : inout
O : output
D : Default Interface
No IO Protocol
Wire handshake protocols
Memory protocols : RAM
: FIFO
Bus protocols
Block Level Protocol
Block level protocols can be applied to the return port - but the port can be omitted and just the function name specified
22- 42

## Slide 43: Bus IO Protocol
Vivado HLS supports a Bus IO protocol
  It is that of a generic bus
    Not an industry standard
  Can be used to communicate with a bus bridge
  The Vivado HLS bus protocol is principally used to connect to adapters
The Bus IO protocol supports memcpy
  The bus IO protocol supports the C function memcpy
  This provides a high performance interface for bursting data in a DMA like fashion
The Bus IO protocol supports complex pointer arithmetic at the IO
  Pointers at the IO can be synthesized to ap_fifo or ap_bus
    If using ap_fifo, the accesses must be sequential
    If pointer arithmetic is used, the port must use ap_bus
22- 43

## Slide 44: Standard and Burst Mode
Standard Mode
  Each access to the bus results in a request then a read or write operation
  Multiple read or writes can be performed in a single transaction
Burst Mode
  Use the memcpy command
  Copies data between array & a pointer argument
  The pointer argument can be a bus interface
    This example uses a size of 4
    This is more efficient for higher values
#include "bus.h"
void foo (int *d) {
int buf1[4], buf2[4];
int i;
memcpy(buf1,d,4*sizeof(int));
for (i=0;i<4;i++) {
buf2[i] = buf1[3-i];
}
memcpy(d,buf2,4*sizeof(int));
}
#include "bus.h"
void foo (int *d) {
static int acc = 0;
int i;
for (i=0;i<4;i++) {
acc += d[i];
d[i] = acc;
}
}
#include "bus.h"
void foo (int *d) {
static int acc = 0;
int i;
for (i=0;i<4;i++) {
acc += *(d+i);
*(d+i) = acc;
}
}
#include "bus.h"
void foo (int *d) {
static int acc = 0;
int i;
acc += d[i];
d[i] = acc;
}
Single read and write in Standard Mode
Multiple reads and writes in Standard Mode
Burst Mode
22- 44

## Slide 45: Bus IO Protocol: Ports Generated
Bus request then access protocol
  The protocol will request a read/write bus access
  Then read or write data in single or burst mode
#include “foo.h"
void foo (int *d) {
…
}
foo
d_dataout[31:0]
d_datain[31:0]
d_req_write
d_rsp_read
d_req_din
d_address[31:0]
d_size[31:0]
d_req_full_n
d_rsp_empty_n
d_rsp_dout
Input Ports | Description
d_datain | Input data.
d_req_full_n | Active low signal indicates the bus bridge is full. The design will stall, waiting to write.
d_rsp_empty_n | Active low signal indicates the bus bridge is empty and can accept data.
Output Ports | Description
d_dataout | Output data.
d_req_write | Asserted to initiate a bus access.
d_req_din | Asserted if the bus access is to write. Remains low if the access it to read.
d_rsp_read | Asserted to start a bus read (completes a bus access request and starts reading data)
d_address | Offset for the base address.
d_size | Indicates the burst (read or write) size.
Standard Mode: The address port gives the index address e.g. *(d+i), addr = value of “i”
22- 45

## Slide 46: Bus IO Protocol (Standard, Read)
void foo (int *d) {
static int acc = 0;
int i;
for (i=0;i<4;i++) {
acc += d[i+1];
d[i] = acc;
}
}
After start, idle goes low and the RTL operates until a read is required
A req_write high with req_din low indicates a read request
A read address is supplied: value is the pointer index value
The RTL will stall (wait) until the empty_n is asserted high to indicate data is available
As soon as data is available, rsp_read will go high
Reads will occur when required, so long as data is available (empty_n is high)
22- 46

## Slide 47: Bus IO Protocol (Standard, Write)
After start, idle goes low and the RTL operates until a write is required
When a write is required, data and address are applied
The RTL will stall (wait) until the full_n is asserted high to indicate space is available
As soon as data is available, rsp_write and req-din will go high
A req_write high with req_din high indicates a write request
There is no acknowledge for writes in this interace
Write will occur when required, so long as data is available (full_n is high)
22- 47
void foo (int *d) {
static int acc = 0;
int i;
for (i=0;i<4;i++) {
acc += d[i+1];
d[i] = acc;
}
}

## Slide 48: Bus IO Protocol (Burst, Read)
Similar to a Standard Mode
This example uses a burst=4
The base address is zero
The burst size is placed on port size
All reads are done consecutively
The empty_n signal will stall the RTL until data is available
22- 48
void foo (int *d) {
int buf1[4], buf2[4];
int i;
memcpy(buf1,d,4*sizeof(int));
for (i=0;i<4;i++) {
buf2[i] = buf1[3-i];
}
memcpy(d,buf2,4*sizeof(int));
}

## Slide 49: Bus IO Protocol (Burst, Write)
Similar to a Standard Mode
This example uses a burst=4
The base address is zero
The burst size is placed on port size
All writes are done consecutively
The full_n signal will stall the RTL until data is available
22- 49
void foo (int *d) {
int buf1[4], buf2[4];
int i;
memcpy(buf1,d,4*sizeof(int));
for (i=0;i<4;i++) {
buf2[i] = buf1[3-i];
}
memcpy(d,buf2,4*sizeof(int));
}

## Slide 50: Outline
Introduction
Block Level Protocols
Port Level Protocols
Summary

## Slide 51: Summary
Vivado HLS has four types of IO
  Data ports created by the original C function arguments
  IO protocol signals added at the Block-Level
  IO protocol signals added at the Port-Level
  IO protocol signals added externally as Pcore Interfaces
Block Level protocols provide default handshake
  Block Level handshakes are added to the RTL design
  Enables system level control & sequencing
Port Level Protocols provide wide support for all standard IO protocols
  The protocol is dependent on the C variable type